## Slide 1
Previous Work — Model Training & Weight Extraction
▸ Trained VGG16 on MNIST dataset (~31 MB weights)
▸ Trained GoogLeNet on Fashion-MNIST (~40 MB weights)
▸ Both models saved as PyTorch .pth state dictionaries
▸ Weights include convolution kernels, biases, batch-norm parameters
▸ Python reference model created for Posit<16,1> encoding/decoding
▸ float_to_posit16_1() converts FP32 → 16-bit Posit (ES=1)
posit_encoder.py (Python reference)
def float_to_posit16_1(x):
# 1. Handle sign
sign = 1 if x < 0 else 0
# 2. Compute regime k
# USEED = 2^(2^ES) = 4
k = 0
while x >= USEED: # x >= 4
x /= USEED; k += 1
# 3. Extract exponent bit
exponent = 1 if x >= 2 else 0
# 4. Extract fraction bits
fraction = x - 1
# 5. Pack: sign | regime | exp | frac
return posit_bits

## Slide 2
Previous Work — FP32 to Posit Weight Conversion
VGG16 / GoogLeNet .pth weights (FP32)
convert_convnext_weights.py np.vectorize(float_to_posit16_1)
Posit<16,1> Weights .npy arrays (16-bit integers)
▸ Each FP32 weight/bias is individually converted to a 16-bit Posit<16,1> integer
▸ Conversion uses the Python reference encoder (float_to_posit16_1)
▸ Converted weights are stored in NumPy .npy format, preserving original tensor shapes
▸ check_converted_weights.py verifies conversion accuracy by decoding back to float
▸ These Posit-encoded weights are what the hardware accelerator will load into PEs

## Slide 3
Verilog — Posit Decoder & Encoder
posit_decoder.v — Unpacks N-bit Posit into fields
module posit_decoder #(N=8, ES=1) (
input [N-1:0] posit_in,
output sign, is_zero, is_nar,
output signed [$clog2(N):0] k, // regime value
output [ES-1:0] exponent,
output [N-1:0] fraction,
output [$clog2(N):0] frac_len
);
// Steps:
// 1. Check special cases (zero, NaR)
// 2. Extract sign, 2's complement for negative
// 3. Count regime run-length → k
// 4. Extract exponent bits after regime
// 5. Extract fraction bits (left-justified)
posit_encoder.v — Packs fields back into N-bit Posit
module posit_encoder #(N=8, ES=1) (
input sign, is_zero, is_nar,
input signed [$clog2(N):0] k,
input [ES-1:0] exponent,
input [N-1:0] fraction,
output [N-1:0] posit_out
);
// Steps:
// 1. Handle zero / NaR special outputs
// 2. Build regime bits from k
// k>=0 → (k+1) ones + terminating 0
// k<0 → |k| zeros + terminating 1
// 3. Insert exponent, fraction bits
// 4. Apply sign via 2's complement
Posit<8,1> Bit Layout Example:
S
Regime
E
Fraction
sign | 1...10 (run) | exp bit(s) | mantissa bits

## Slide 4
Verilog — Posit Adder & Multiplier
posit_adder.v (Combinational, ~300 lines)
▸ Decodes both inputs via posit_decoder
▸ Computes unified scale: scale = k × 2^ES + exponent
▸ Builds significands with hidden 1: sig = {1, fraction}
▸ Aligns smaller operand by right-shifting
▸ Adds/subtracts signed significands
▸ Normalizes result (find leading-one, shift)
▸ Decomposes result scale → new k and exponent
▸ Encodes output via posit_encoder
posit_multiplier.v (Combinational, ~325 lines)
▸ Decodes both inputs via posit_decoder
▸ Result sign = sign_a XOR sign_b
▸ Builds mantissas: mant = {1'b1, fraction}
▸ Integer multiply: product = mant_a × mant_b
▸ Scales add: total_scale = scale_a + scale_b
▸ Normalizes: if product MSB set → shift right, scale+1
▸ Trims trailing zeros for frac_len
▸ Saturates k to valid Posit range, encodes output
Common Pattern: Decode → Operate on (sign, scale, significand) → Normalize → Encode
Both are fully combinational (no clk). Each adder/multiplier internally instantiates its own decoder and encoder.

## Slide 5
Verilog — Processing Element (PE)
pe.v — Weight-Stationary, 2-Stage Pipelined MAC
module pe #(N=8, ES=1) (
input clk, reset, pe_en, clear_acc, wshift,
input [N-1:0] input_in, weight_in, psum_in,
output [N-1:0] input_out, psum_out, pe_output
);
// Weight stays frozen (only loads when wshift=1)
always @(posedge clk)
if (wshift) weight_reg <= weight_in;
// Activation slides through (left → right)
always @(posedge clk)
if (pe_en) input_reg <= input_in;
assign input_out = input_reg;
// Stage 1: Multiply (combinational)
posit_multiplier MUL(.a(input_reg),.b(weight_reg),
.out(product_comb));
// Stage 2: Add psum (combinational)
posit_adder ADD(.a(product_reg), .b(psum_pipe_reg),
.out(psum_comb));
// Pipeline registers between stages
always @(posedge clk) begin
product_reg <= product_comb; // stage 1 result
psum_pipe_reg <= psum_in; // matching psum
psum_out_reg <= psum_comb; // stage 2 result
end
PE Dataflow Diagram
Activation In (from left PE)
input_reg
→ Right
weight_reg (stationary)
posit_multiplier
product_reg (pipeline)
psum_in (from above)
posit_adder
psum_out ↓

## Slide 6
Verilog — 6×6 Weight-Stationary Systolic Array
▸ systolic_array.v generates a ROWS×COLS grid of PEs
▸ Activations flow horizontally (left → right) via act_bus
▸ Partial sums flow vertically (top → bottom) via psum_bus
▸ Top row psum_in initialized to zero
▸ Bottom row psum_out = final column results
▸ Weights loaded in parallel via wshift before computation
▸ All PEs share clk, reset, pe_en, clear_acc signals
systolic_core.v wraps the array with:
▸ Input FIFOs — per-row buffers for activation skewing
▸ Row delay registers — stagger activations diagonally
▸ Output delay registers — de-skew the column results
▸ This ensures correct data alignment across the pipeline
Array Layout (6×6 PE Grid):
Act[0]→
PE [0,0]
PE [0,1]
PE [0,2]
PE [0,3]
Act[1]→
PE [1,0]
PE [1,1]
PE [1,2]
PE [1,3]
Act[2]→
PE [2,0]
PE [2,1]
PE [2,2]
PE [2,3]
Act[3]→
PE [3,0]
PE [3,1]
PE [3,2]
PE [3,3]
↓
↓
↓
↓
psum_out (final results per column)
Quire variants (pe_quire.v, systolic_array_quire.v) accumulate in a 128-bit fixed-point quire register for zero rounding error during MAC accumulation.

## Slide 7
Current Status & Next Steps
✅ Completed
▸ Posit<16,1> Python reference encoder & decoder
▸ Model training (VGG16, GoogLeNet) and weight extraction
▸ FP32 → Posit weight conversion pipeline
▸ Verilog posit_decoder — bit unpacking
▸ Verilog posit_encoder — bit packing
▸ Verilog posit_adder — full posit addition
▸ Verilog posit_multiplier — full posit multiplication
▸ Verilog PE — 2-stage pipelined weight-stationary PE
▸ Verilog PE Quire — PE with 128-bit quire accumulation
▸ Verilog 6×6 Systolic Array (standard + quire variants)
▸ Verilog Systolic Core with input FIFOs and skewing logic
▸ Testbenches written for all modules
🔲 Next Steps
▸ Run & verify all testbenches (PE, Systolic Array)
▸ Analyze simulation waveforms for timing correctness
▸ Build top-level controller / FSM for the accelerator
▸ Implement layer-level dataflow (tiling, feature maps)
▸ Load converted Posit weights into systolic array
▸ End-to-end inference test with MNIST/FMNIST images
▸ FPGA synthesis and resource utilization analysis
▸ Performance benchmarking vs FP32 / INT8 baselines